## Slide 1: Programming Arduino and Nano 33 BLE

## Slide 2: Contents
Programming Arduino and Nano 33 BLE

## Slide 3: aRDUINO
Arduino’s purpose is to control things by interfacing with sensors and actuators
  No keyboard, mouse and screen
  Can be attached via “shields”
  No operating system, limited memory
  A single program enjoys 100% of CPU time
Physical Arduino boards
  Uno
  Nano
  Leonardo
  Mega
  Pro Mini
Arduino IDE
  Installed on a PC (Windows/Mac/Linux)
  To develop, install and debug programs on Arduino boards
  Communicates with Arduino board over USB
Third party Arduino compatible boards
  STM32
  Nucleo / Discovery / Feather,
  Adafruit
  SparkFun

## Slide 4: aRDUINO
A generic AVR microcontroller block diagram
  CPU
  Internal Memory
    Flash (stores program code)
    SRAM (holds data and variable during execution)
    EEPROM (holds persistent data generated by program)
  Peripherals
    A/D converter (ADC)
    Timers
    UART
    SPI
    DMA
    GPIO
    TWI
    Comparator
    RTC
    WDT
    RNG

## Slide 5: aRDUINO
Interfacing with Arduino
  Temperature sensor
  Pressure sensor
  Switches
  Variable resistor
  Range finder
  PIR (person
  in room) sensor
  Relay
  Motor control
  LED
  16x2 display
  Graphic display
  Bluetooth shield
  WiFi
  shield
  Ethernet shield
Arduino Libraries:
https://www.arduinolibraries.info/libraries

## Slide 6: aRDUINO
Uno vs Nano 33 BLE Sense

## Slide 7: aRDUINO
Features of Nano 33 Sense
  8 Analog Input Pins can provide 12-bit ADC at about 30 kHz
  Integrated sensors (IMU, Mic, Light, Pressure, Temperature, Humidity)
  All digital pins can trigger interrupts
  Only supports 3.3V I/Os and is NOT 5V tolerant so please make sure you are not directly connecting 5V signals to this board or it will be damaged

## Slide 8: Nano 33 Sense
Nano 33 Sense

## Slide 9: Nano 33 Sense
Nano 33 Sense

## Slide 10: Nano 33 Sense
Arduino Nano comparisons

## Slide 11: Nano 33 Sense
Pinout

## Slide 12: Nano 33 Sense
Nano 33 BLE Power Tree

## Slide 13: Nano 33 Sense
nRF52840
  Arduino Nano BLE (and BLE Sense) is based on the nRF52840 microprocessor made by Nordic
  nRF52840 has the ARM Cortex M4 processor with single precision floating point unit (FPU)
  The nRF52840 contains 1 MB of flash and 256 kB of RAM that can be used for code and data storage
  The flash can be read an unlimited number of times by the CPU, but it has restrictions on the number of times it can be written and erased (minimum 10,000 times) and also on how it can be written
  The flash is divided into 256 pages of 4 kB each that can be accessed by the CPU via both the ICODE and DCODE buses

## Slide 14: Nano 33 Sense
Arduino Sketch Structure

## Slide 15: Nano 33 Sense
Arduino Sketch Example

## Slide 16: Nano 33 Sense
Arduino Sketch Example

## Slide 17: Nano 33 Sense
Read form serial
https://www.arduino.cc/reference/en/

## Slide 18: Nano 33 Sense
Length of data type may be different on different CPUs

## Slide 19: Nano 33 Sense
Arduino Pin Names
  Pin name aliases are defined in the pins_arduino.h
  As a convention
  Digital pins can be referred by the number (e.g., 3) or D+number (e.g. D3)
  Analog pins must be referred by A+number , e.g., A3

## Slide 20: Nano 33 Sense
Arduino Sketch Example
To test, connect a jumper cable to A2, and try connecting the other end to 3.3 V or GND, and observe the output in the Serial Monitor

## Slide 21: Nano 33 Sense
Arduino Sketch Example

## Slide 22: Nano 33 Sense
Integer vs Floating point arithmetic

## Slide 23: Nano 33 Sense
Bitwise operation

## Slide 24: Nano 33 Sense
Endianness and byte addressing
  Beware of the endianness when you need to manipulate or transmit data by bytes, or when memory contents are transmitted between computers with different endianness
  Casting an uint32_t integer to uint8_t takes the low 8-bit of the integer

## Slide 25: Nano 33 Sense
Pulse Width Modulation (PWM)
  A technique for getting analog results with digital means
  Digital control is used to create a square wave, a signal switched between ON and OFF
  The simulated analog voltage is the portion of the time the signal spends ON versus the time that the signal spends OFF
https://docs.arduino.cc/learn/microcontrollers/analog output

## Slide 26: Nano 33 Sense
PWM Frequency and Pins

## Slide 27: Nano 33 Sense
PWM example (use PWM to fade LED)
  Examples--> 01. Basics --> Fade

## Slide 28: Nano 33 Sense
Two-wire serial communication toy example
  Serial interface is common in device communications
    Send / Receive data one bit at a time
    Need a clock signal to synchronize timing between sending and receiving ends
  Sender does this to send a byte:
    Set the data pin to the first bit (MSB) of the byte to be sent
    Wait for the signal to be stable
    Pulse the clock pin
    Repeat step 1 for the next bit until all 8 bits are sent

## Slide 29: Nano 33 Sense
Two-wire serial communication toy example
  Serial interface is common in device communications
    Send / Receive data one bit at a time
    Need a clock signal to synchronize timing between sending and receiving ends
  Sender does this to send a byte:
    Set the data pin to the first bit (MSB) of the byte to be sent
    Wait for the signal to be stable
    Pulse the clock pin
    Repeat step 1 for the next bit until all 8 bits are sent

## Slide 30: Nano 33 Sense
Two-wire serial send (tx) example

## Slide 31: Nano 33 Sense
Two-wire serial receive (rx) example

## Slide 32: Nano 33 Sense
Two-wire serial communication
  Upload the Tx code to the sender board, upload Rx code to the receiver board
    Make sure two boards have the same I/O voltage
    e.g., don’t connect Uno (5v) with Nano (3.3v)
  Connect the sender and receiver
    sender’s dataPin --> receiver’s dataPin
    sender’s clockPin --> receiver’s clockPin
  Open the Serial Monitor on the receiver end to see data received
  CAUTION
    Don’t upload the sender code to both boards and connect them
    Can damage boards when two digital output pins connect

## Slide 33: Nano 33 Sense
I2C Interface
  I2C is a serial communication protocol, commonly used for connecting MCU and sensors
  It is a “bus”, meaning multiple devices can use the same two wires (one for timing, one for data)
  In other words, the MCU can use only two wires to communicate with multiple (up to 127) devices (i.e., sensors)

## Slide 34: Nano 33 Sense
I2C Interface
  The device that provides the clock signal is the “master”, all others are “slaves”
    Typically, the MCU is the master, sensor units are slaves
    Each slave connected on the bus should have a unique address, which is a number between 1 and 127
      The value 0 is the broadcast address
    The master identifies the slave by the slave’s address
    For a sensor unit, its I2C address is typically hardcoded, and is explained in the datasheet

## Slide 35: Nano 33 Sense
I2C hardware
  I2C uses two wires (thus, also called two wire interface, or TWI): Serial Clock (SCL) line and Serial Data (SDA) line
  When no data is transmitted, SCL and SDA lines are in a tri state or free state, i.e., neither HIGH nor LOW, a floating value
  When there is data to be transmitted, the sender (master or slave) takes the SDA line out of tri state and sends data as logic highs and lows in time with the clock signal
  When transmission is complete, the clock signal can stop, and the SDA line is returned to tri state
  Usually the slave only sends data upon the master’s request, so the clock signal is guaranteed available

## Slide 36: Nano 33 Sense
I2C Library
  On Arduino, the Wire library provides functions for I2C communication
    https://www.arduino.cc/reference/en/language/functions/communication/wire/begin
    https://www.arduino.cc/reference/en/language/functions/communication/wire/end
    https://www.arduino.cc/reference/en/language/functions/communication/wire/requestfrom
    https://www.arduino.cc/reference/en/language/functions/communication/wire/begintransmission
    https://www.arduino.cc/reference/en/language/functions/communication/wire/endtransmission
    https://www.arduino.cc/reference/en/language/functions/communication/wire/write
    https://www.arduino.cc/reference/en/language/functions/communication/wire/available
    https://www.arduino.cc/reference/en/language/functions/communication/wire/read
    https://www.arduino.cc/reference/en/language/functions/communication/wire/setclock
    https://www.arduino.cc/reference/en/language/functions/communication/wire/onreceive
    https://www.arduino.cc/reference/en/language/functions/communication/wire/onrequest
    https://www.arduino.cc/reference/en/language/functions/communication/wire/setwiretimeout
    https://www.arduino.cc/reference/en/language/functions/communication/wire/clearwiretimeoutflag
    https://www.arduino.cc/reference/en/language/functions/communication/wire/getwiretimeoutflag

## Slide 37: Nano 33 Sense
I2C experiments
  Connect two Arduino Nano 33 BLE boards via I2C
  One acts as master and the other acts as slave

## Slide 38: Nano 33 Sense
UART Protocol
  UART (Universal asynchronous receiver transmitter) is
    A device to device communication protocol
    A block of circuitry responsible for implementing serial communication (hardware UART)
https://www.analog.com/en/analog-dialogue/articles/uart-a-hardware-communication-protocol.html
https://learn.sparkfun.com/tutorials/serial-communication/rules-of-serial

## Slide 39: Nano 33 Sense
UART Protocol
  The interface can be bit banged, i.e., directly controlled by the processor, called Software UART
  Processor intensive, not preferred but does the job when hardware UART is not available
  Baud rate must be set the same on both ends of the communication channel
  Most typical Baud Rates: 9600 , 19200, 38400, 57600, 115200 , 230400, 460800, 921600, 1000000, 1500000

## Slide 40: Nano 33 Sense
BLESerial on Nano 33 BLE

## Slide 41: Nano 33 Sense
BLESerial on Nano 33 BLE
  Install the HardwareBLESerial library
  Upload the code to Nano 33 BLE
    Modify “IE5995” to something else before uploading, to prevent conflicts
  Download the phone app “Bluefruit Connect”
    Via App Store or Google Play
  Connect to the device via Bluefruit Connect
  Open UART in Bluefruit Connect
  Open Serial Monitor of the PC that’s connected to Nano 33 BLE
  You can exchange text messages between the Serial Monitor on PC and the UART console in Bluefruit Connect on the cellphone

## Slide 42: Nano 33 Sense
BLESerial on Nano 33 BLE

## Slide 43: Nano 33 Sense
Interrupts
  Interrupts allow microcontrollers to respond to events without having to repeatedly poll to see if the event has occurred
  Interrupts can be triggered by a Pin or by a Timer

## Slide 44: Nano 33 Sense
Interrupts
  Interrupt Handling Process

## Slide 45: Nano 33 Sense
Interrupts
  Example

## Slide 46: Nano 33 Sense
Interrupts
  Pins available for interrupts

## Slide 47: Nano 33 Sense
Arduino code optimization for speed
  Avoid using float
    Floating point arithmetic is slow on hardware that does not support it
    Use long instead, which can retain more digits of precision, and faster
  Lookup rather than calculate
  Use const byte instead of int for small constants such as Pin names
  Move looping code into the setup function
    The loop() function checks for Serial communication which takes time
  Speeding up Digital IO
    Directly manipulate the pin bit in the port register
  Speeding up Analog Inputs
    Reducing the prescaler of the Timer that triggers ADC conversions

## Slide 48: Nano 33 Sense
Arduino code optimization for speed

## Slide 49: Nano 33 Sense
Minimize power usage
  If the product is battery operated, reducing power usage is important
  Ways to reduce power consumption
    Put the microcontroller in sleep when it is not doing anything
    Turn off (disable) unused peripherals
    Use lowest clock frequency sufficient
    Use lower input voltage if allowable
    Provide power to sensor only when taking a reading

## Slide 50: Nano 33 Sense
Minimize RAM usage
  Reduce the amount of memory used by data and variables
    Choose data type based on need, especially for large arrays
      Int is at least 2 byte, values range in [ 32,768, 32767]
      If the value range of [0, 255] suffices, use byte , which is 1 byte
    Store string constants in Flash Memory
      Serial.println(“Some message to print”); // Stored both in flash memory and in RAM
      Serial.println(F (“Some message to print”)); // Fetched from flash memory, no RAM use
    Use PROGMEM directive to store constant arrays in Flash
      #include <avr/pgmspace.h>
    Use const if the variable value do not change while the sketch is running
      “const int v = 5000;” uses less memory than “int v = 5000;” and runs faster when v is used in computation
    Bypass the bootloader
      The Nano 33 BLE bootloader takes 35 KB of Flash Memory
      There is a way to program the chip without using a bootloader, thus saving RAM and reducing start-up time
    Length of variable names does not help save memory

## Slide 51: Nano 33 Sense
Integrated sensors on Nano 33 BLE Sense

## Slide 52: Nano 33 Sense
Integrated sensors on Nano 33 BLE Sense
  LSM9DS1
    The LSM9DS1 inertial measurement unit (IMU)
      accelerometer
      gyroscope
      magnetometer
    Useful for detecting orientation, motion or vibrations
    Datasheet: https://content.arduino.cc/assets/Nano_BLE_Sense_lsm9ds1.pdf
    Library “Arduino_LSM9DS1”

## Slide 53: Nano 33 Sense
Integrated sensors on Nano 33 BLE Sense
  LSM9DS1

## Slide 54: Nano 33 Sense
Interact with sensors on the I2C bus
  There are ready made libraries to read sensor data from the integrated sensors on the BLE Sense board
  For the sake of learning, let us implement our own “device driver” to obtain sensor data
  We will start with the barometric pressure sensor LPS22HB

## Slide 55: Nano 33 Sense
Interact with sensors on the I2C bus
  Write your own device driver for LPS22HB
    First, find out how LPS22HB is physically connected to the nrf52840 MCU on the BLE Sense Rev2 board

## Slide 56: Nano 33 Sense
Interact with sensors on the I2C bus
  Write your own device driver for LPS22HB
    Next, find the datasheet of LPS22HB and go to the I2C operation section

## Slide 57: Nano 33 Sense
Interact with sensors on the I2C bus
  Write your own device driver for LPS22HB
    When we need the sensor to acquire a new reading, we need to set the least significant bit (bit 0) of the CTRL_REG2 register

## Slide 58: Nano 33 Sense
Interact with sensors on the I2C bus
  Write your own device driver for LPS22HB
    The pressure data is 24 bit; thus we need to read the three 8 bit registers (at addresses 0x28, 0x29 and 0x2A)
    If IF_ADD_INC bit is set in CTRL_REG2, then register address will be automatically incremented in repeated read of multi byte data

## Slide 59: Nano 33 Sense
Interact with sensors on the I2C bus
  Write your own device driver for LPS22HB
    The temperature is 16 bit value, contained in two registers

## Slide 60: Nano 33 Sense
Interact with sensors on the I2C bus
  Write your own device driver for LPS22HB
    Trigger a conversion

## Slide 61: Nano 33 Sense
Interact with sensors on the I2C bus
  Write your own device driver for LPS22HB
    Check if data is ready, before reading

## Slide 62: Nano 33 Sense
Interact with sensors on the I2C bus
  Write your own device driver for LPS22HB
    Read data

## Slide 63: Nano 33 Sense
Interact with sensors on the I2C bus
  Write your own device driver for LPS22HB
    Read data

## Slide 64: Nano 33 Sense
Interact with sensors on the I2C bus
  Write your own device driver for LPS22HB
    Complete code:

## Slide 65
20ms
5ms